## Slide 1: Numerical Challenges in Efficient Modeling of Colliding Flows
Scott Feister
Postdoc, University of Chicago
OSIRIS Users and Developers Workshop
September 19, 2017

## Slide 2: Outline
Discuss new user experience
Technical challenges modeling impinging flows

## Slide 3: Introduction: A new user to OSIRIS
Workflow:
  Decks:
    Git repo for each simulation; contains decks and analysis
  Run:
    BlueGene/Q and/or Intel supercomputers (hundreds to millions of cores)
  Analysis:
    Python, Matplotlib, Mpi4py
Learning OSIRIS syntax, boundary conditions, etc.:
  Ask Ben Winjum (documentation M.I.A.!)

## Slide 4: Uses of OSIRIS
Instability growth at interface of impinging flows
Other interests:
  Passing state between FLASH and OSIRIS
  LWFA
  High-intensity laser interactions with solids/liquids

## Slide 5: Goal: Study the interface of colliding flows
Region of interest
Material A
Material B
Interaction region takes a while to develop… how to efficiently simulate?

## Slide 6: Original deck: Computationally expensive reservoir!
Reservoir
Material A
Material B
Interaction region takes a while to develop… requiring larger and larger reservoirs!
Reservoir
Region of interest

## Slide 7: More efficient: don’t model the reservoir particles!
Inflow boundary
Inflow boundary

## Slide 8: One hitch! I couldn’t get a steady state flow with this test problem… can you?
Inflow
(protons + electrons)
Outflow
Filamentation instabilities engulfed the flow.
TEST PROBLEM

## Slide 9: Optimized BG/Q: Introduces numerical instability?
qsub -t $WALLMIN -n 256 --proccount 4096 --mode c16 -A $PROJECT osiris-2D.e input_file
Workaround: I commented out the "SIMD = BGQ" line of compilation as well as changing to SINGLE precision.
Consequence: No instability, but code runs half as fast.

## Slide 10: Going back to reservoir scheme, an instability at the boundaries

## Slide 11
Problem: No boundary conditions avoid instability as plasma flow away from edges.
Workaround: Tapered density profile near boundaries.
Instability is from lost electrons at edges

## Slide 12: Duct tape solution: taper density near the edges
Density tapers off at top/bottom edges
Density is constant right up to top/bottom edges
WHY? In part, because target charges up when thermal electrons stick to top/bottom walls.
AFTER
BEFORE
Noise obstructs signal
Signal is clear

## Slide 13: Conclusion
Glad to be a new member of the OSIRIS user community!
Looking forward to Anton’s talk on documentation
Has anyone implemented a stable “inflow” neutral plasma boundary?
Inflow
(protons + electrons)
Outflow